## Slide 1: Kratos Multiphysics Fluid Dynamics Application Tutorial
4th Kratos Multiphysics workshop
Rubén Zorrilla
Jordi Cotela
Riccardo Rossi
Javier Gárate

## Slide 2
Kratos Multiphysics Fluid Dynamics Application Tutorial 0. 100 Re cylinder case
v = 0
v = 0
p = 0
vcyl = 0
v = vin
Fluid properties:
ρ = 1.0 kg/m³
μ = 0.002 kg/m·s
Inlet profile:
vx,in = 6y(1-y)sin(πt/2) if t < 1
vx,in = 6y(1-y) if t ≥ 1
Time settings:
Δt = 0.1 s
Tend = 45 s

## Slide 3
Kratos Multiphysics Fluid Dynamics Application Tutorial 1. Select Fluid Dynamics Application
Load the Kratos problem type: Data  Problem type  Kratos
1. Select Fluid Dynamics Application
2. Select body fitted CFD
3. Select problem size (2D)

## Slide 4
Kratos Multiphysics Fluid Dynamics Application Tutorial 2. Draw geometry and set groups
Draw the channel + cylinder geometry:
Draw the channel boundaries
Draw the immersed cylinder
Remove all surfaces
Set a surface using the channel + cylinder boundaries
Set the required groups:
Inlet: left edge (1 line)
Outlet: right edge (1 line)
No_Slip_Walls: top and bottom edges (2 lines)
No_Slip_Cylinder: cylinder boundary (1 line)
Fluid: fluid domain surface (1 surface)

## Slide 5
Kratos Multiphysics Fluid Dynamics Application Tutorial 2. Draw geometry and set groups

## Slide 6
Kratos Multiphysics Fluid Dynamics Application Tutorial 3. Formulation and properties
Select formulation:
Analysis type  Solution strategy: Monolithic
Parts (fluid domain and properties):
Set properties (ρ, μ)
Apply to the Fluid group
NOTE: Only one part is allowed, meaning that all the surfaces (volumes) that conform the fluid domain must be stored in a unique group

## Slide 7
Kratos Multiphysics Fluid Dynamics Application Tutorial 4. Time intervals
Create time intervals:
Set the time intervals to apply the problem BCs.
To create a new time interval:
Right click over “Time intervals”
Click “Create new interval”
Fill the time interval data
In this case:
inlet1: Start time: 0.0 // End time: 1.0
inlet2: Start time: 1.0 // End time: “End” (string)

## Slide 8
Kratos Multiphysics Fluid Dynamics Application Tutorial 5. Boundary conditions
Inlet (t < 1):
Inside the Conditions tab:
Double click “Automatic inlet velocity”
Select “by function” option
Introduce the first velocity function:
  6*y*(1-y)*sin(0.5*pi*t)
Set the time interval from 0.0 to 1.0 (inlet1)
Apply to the Inlet group
NOTE: Any Python compiled function depending on x, y, z and t can be introduced.

## Slide 9
Kratos Multiphysics Fluid Dynamics Application Tutorial 5. Boundary conditions
Inlet (t ≥ 1):
Inside the Conditions tab:
Double click “Automatic inlet velocity”
Select “by function” option
Introduce the second velocity function
  6*y*(1-y)
Set the time interval from 1.0 to “End” (inlet2)
Apply to the Inlet group
NOTE: Any Python compiled function depending on x, y, z and t can be introduced.

## Slide 10
Kratos Multiphysics Fluid Dynamics Application Tutorial 5. Boundary conditions
Outlet:
Inside the Conditions tab:
Double click “Outlet”
Set value to 0.0
Apply to the Outlet group

## Slide 11
Kratos Multiphysics Fluid Dynamics Application Tutorial 5. Boundary conditions
No slip:
Inside the Conditions tab:
a) Cylinder
Double click “No slip”
Apply to the No_Slip_Cylinder group
b) Walls
Double click “No slip”
Apply to the No_Slip_Walls group

## Slide 12
Kratos Multiphysics Fluid Dynamics Application Tutorial 6. Solver and time settings
Inside the Solution tab:
Solver settings:
a) Parallel configuration: OpenMP / MPI
b) Strategy parameters: Defaults are OK
c) Linear solver: Let Kratos select the suitable one
Time settings:
Set “Start time” to 0.0
Set “End time” to 45.0
Set “Delta time” to 0.1
(“Automatic delta time” can be used instead)

## Slide 13
Kratos Multiphysics Fluid Dynamics Application Tutorial 7. Post-process settings
Inside the Results tab:
Output type:
a) Output unit: Steps / time
b) Frequency: 1.0 (each step)
Output variables: velocity and pressure
Drag computation:
a) Time interval: Total
b) Drag group: No_Slip_Cylinder

## Slide 14
Kratos Multiphysics Fluid Dynamics Application Tutorial 8. Mesh & solve

## Slide 15
Kratos Multiphysics Fluid Dynamics Application Tutorial 9. Results

## Slide 16
Kratos Multiphysics Fluid Dynamics Application Tutorial
The presented example can be automatically reproduced by clicking in this icon.

## Slide 17
THANK YOU