## Slide 1: GENERAL VIEW OF KRATOS MULTIPHYSICS
An introduction to design philosophy

## Slide 2: Introduction Outlook
Design principles
  What can Kratos do for you?
The description of the model
  Our implementation of a finite element discretization.
Simulating a problem
  Components of a solution algorithm.
Global workflow
  How can we use all this?

## Slide 3: Design principles Goals
Framework for the simulation of finite element problems
  Flexible
  Extensible
  Reusable
  Efficient

## Slide 4: Design principles Intended users
Finite element developers
  Advanced mathematical or engineering background.
  Basic computer science knowledge.
Software developers
  Expert programmers.
  Can be interested in using Kratos as a piece in a wider project.
Package users
  Engineers and designers.
  Use Kratos as a black box.
  Not interested in implementation details or internal structure.
Notes: As I removed the previous slide, mention that Kratos is a framework for the solution of finite element problems

## Slide 5: Design Principles General design
Object-Oriented design
  Problem is divided into separate objects.
  An interface defines the interaction between components.
  Objects based on common FE concepts.
C++ programming language
  Supports object oriented design.
  High performance code.
Multi-layered approach
  Distinction between basic and high-level code.
Notes: Each component holds its own data

## Slide 6: General Structure Objects
Numerical solutions
FE Methodology
Library interfaces
FEM Algorithms
FE Modeling

## Slide 7: General Structure Layers
Easy Advanced programming
Dependency
Kratos internals
Extensions

## Slide 8: General Structure Kernel and Applications
Kratos
Fluid Dynamics
Structural Mechanics
PFEM
Fluid-Structure Interaction
Numerical and programming core
Physics of the problem
Applications can depend on other applications
Kernel coordinates applications
Separate the numerical core and the physics
Development of applications is independent
Notes: The important point here is the last two bullet points

## Slide 9: Components of a model

## Slide 10: Data Structure Nodes and Variables
The node class manages the information related to a single point of the mesh
  ID unique identifier for the node
  Coordinates Position in space
  Nodal Data Problem-related values
ID
Coordinates
Nodal Data
Node
157
X = 5.2
Y = 0.5
Z = 2.0
The Node:

## Slide 11: Data Structure Nodes and Variables
All data is stored in Variable-Value pairs
  Variables are denoted by an uppercase label.
  Kratos defines some variables by itself.
  Applications can define their own variables.
ID
Coordinates
Nodal Data
Node
VELOCITY?
PRESSURE?
u
12,5
Notes: To define variables: Associate a name with a type (vector, scalar, matrix)

## Slide 12: Data Structure Nodal Data
tn-1
Historical database
  Variables tied to the advancement in time.
  Value stored for current time step, as well as previous steps.
  Optimized.
un-1
tn
un
tn-2
un-2
tn+1
un+1
Now
Now

## Slide 13: Data Structure Nodal Data
Non-historical database
  Single value stored at all times.
  Not tied to time iteration.
Degree of freedom / Dof
  Tracks the problem unknowns.
  Position in global system.
  Fixity status: Free (unknown) or Fixed (boundary condition).

## Slide 14: Data Structure Elements and Conditions
Hold the information for a single finite element
Conditions represent element faces
  Used to implement boundary conditions
Calculate local contributions to system
  Mass Matrix
  Damping
  Stiffness
  Right hand side vector
Notes: Elements and conditions concentrate most of the physics of the problem

## Slide 15: Data Structure Elements and Conditions
ID
Elemental Data
Element
Calculate system contributions
Me u’’e + De u’e + Ke ue = fe
Nodes
Shape Functions
Area, Jacobian, …
Geometry
Material properties
Properties
Notes: Elemental and conditional data is Non-historical only

## Slide 16: Data Structure Organization of Data
Each entity stores its data
Properties acts like a shared data between different elements and conditions

## Slide 17: Data Structure Containers
Entities sorted by ID
Fast iteration

## Slide 18: Data Structure Mesh
Mesh stores an arbitrary set of nodes, elements and conditions

## Slide 19: Data Structure Model Part
ModelPart holds the ProcessInfo, variable list and communicator

## Slide 20
Keeps Coherency between fathers and sub model parts
Adding an entity to the child class also adds it to the parents
Removing from parent will remove it from all child
Each sub has a pointer to the same entity in the parent
ModelPart
“Fluid”
ModelPart
“Walls”
ModelPart
“Inlet”
ModelPart
“Outlet”
ModelPart
“Channel”
ModelPart
“Inlet”
Data Structure Sub Model Part

## Slide 21: Simulating a problem

## Slide 22: Solution Strategy Building blocks
Multi-layered approach, with different layers performing independent tasks.
Scheme
  Implements time discretization
  Collects local contributions of Elements and Conditions
  Responsible for updating the system after the solution
Builder and Solver
  Collects local contributions from scheme and assembles them in the global system matrix
  Uses a linear solver to solve the system
  Builder and solver is the main level where to add parallelization
Strategy
  Top solution layer, controls the flow of the problem
  Iterates until convergence, decides when to advance in time

## Slide 23: Solution Strategy Building blocks
Local system contributions
Me u’’e + De u’e + Ke ue = fe
Time-discrete problem
Ae ue = be
Global system
A u = b
Solution iterations
A Δu = b – A u
Time Scheme
Builder and Solver
Strategy
Implements time discretization
Collects contributions from elements and conditions
Updates the unknowns after solution
Finite element assembly
Uses a linear solver to solve the system
Main level where to add parallelization
Controls the flow of the problem
Iterates until convergence

## Slide 24: Solution Strategy Process and Utility
Process
  Generic object used to implement non-standard parts of the solution process.
  Perform a specific task on Execute()
Utility
  Collection of tools to perform a particular task.

## Slide 25: Solution Strategy Python Scripts
The different objects described up to now are implemented as a C++ library.
The solution process is controlled by a Python script.
Solver is the python object in charge of solution of specific physical phenomena
AnalysisStage is the “main” script

## Slide 26: Global workflow

## Slide 27: Global Workflow Overview
Information about the model is read from an input file
  Nodes
  Elements
  Conditions
  Nodal data
  Elemental and conditional data
A Python script drives the solution process
  Import Kratos
  Import and initialize solvers
  Iterate over time

## Slide 28: Global Workflow Input File
Property list
Begin Properties 0
End Properties
Begin Properties 1
DENSITY 2700.00
YOUNG_MODULUS 7000000.00
POISSON_RATIO 0.300
End Properties
Begin Properties 2
...
End Properties
Different Properties can define different parameters and values

## Slide 29: Global Workflow Input File
List of nodes
Begin Nodes
1 2.00000e+00 0.00000e+00 0.00000e+00
2 1.99751e+00 9.96918e-02 0.00000e+00
3 1.90000e+00 0.00000e+00 0.00000e+00
...
703 -1.99751e+00 9.96918e-02 0.00000e+00
704 -2.00000e+00 0.00000e+00 0.00000e+00
End Nodes
X
ID
Y
Z

## Slide 30: Global Workflow Input File
List of elements
Begin Elements FractionalStep2D
1 0 479 513 480
2 0 513 515 480
3 0 476 511 479
...
1259 0 3 1 4
1260 0 1 2 4
End Elements
ID
Element name
Property index
Connectivity

## Slide 31: Global Workflow Input File
List of conditions
Begin Conditions WallCondition2D
1 0 103 104
2 0 104 106
3 0 106 107
...
145 0 63 79
146 0 79 103
End Conditions
ID
Condition name
Property index
Connectivity

## Slide 32: Global Workflow Input File
Nodal Data
Begin NodalData DISPLACEMENT_X
1 1 0.00000e+00
2 1 0.00000e+00
3 1 0.00000e+00
...
703 1 0.00000e+00
704 1 0.00000e+00
End NodalData
Node ID
Kratos Variable
Fixity
Value
Nodal data is stored in the historical database

## Slide 33: Global Workflow Input File
Elemental data
Begin ElementalData C_SMAGORINSKY
1 0.10
2 0.10
3 0.10
...
125 0.10
126 0.10
End ConditionalData
Element ID
Kratos Variable
Value

## Slide 34: Global Workflow Input File
Conditional data
Begin ConditionalData IS_STRUCTURE
1 1.00000e+00
2 1.00000e+00
3 1.00000e+00
...
125 1.00000e+00
126 1.00000e+00
End ConditionalData
Condition ID
Kratos Variable
Value

## Slide 35: Sub Model Parts
sub model parts
Begin SubModelPart Inlets
Begin SubModelPartTables
1
End SubModelPartTables
Begin SubModelPartNodes
2
End SubModelPartNodes
Begin SubModelPartElements
End SubModelPartElements
Begin SubModelPartConditions
1
1800
End SubModelPartConditions
Begin SubModelPart Inlet1
...
End SubModelPart
End SubModelPart
ModelPart
“Fluid”
ModelPart
“Walls”
ModelPart
“Inlet”
ModelPart
“Outlet”
ModelPart
“Channel”
ModelPart
“Inlet”

## Slide 36: JSON Parameters
Parameter class For Configuration
Read JSON
Check for option accepted by solver
Gives method for retrieving the values
{
"problem_data" : {
"problem_name" : "cantilever_selfweight",
"model_part_name" : "Structure",
"domain_size" : 3,
"time_step" : 1.1,
"start_time" : 0.0,
"end_time" : 1.0,
"echo_level" : 0
},
"solver_settings" : {
"solver_type" : "solid_mechanics_static_solver",
"echo_level" : 0,
"solution_type" : "Static",
"analysis_type" : "Linear",
"model_import_settings" : {
"input_type" : "mdpa",
"input_filename" : "cantilever_selfweight"
},
...

## Slide 37
Thank you for your attention!
https://github.com/KratosMultiphysics/Kratos